## Slide 1: Health, Safety & Environmental Management Systems HMAC Orientation and Awareness Training
Wellsboro Plant
Notes: 07/28/26
<number>
Last Update: 4/3/08

## Slide 2: Welcome to HMAC
07/28/26
<number>
Each day you enter you are required to sign in and upon the completion of the day’s activities sign out.
HMAC facilities are “Tobacco Free” facilities.
  See your HMAC contact for designated areas.

## Slide 3: Safety Information Wall
07/28/26
<number>
Wellsboro Plant

## Slide 4: In the Event of an Emergency
07/28/26
<number>
If the need arises for a Plant Evacuation
  Alarm system will Activate
  Leave the nearest Exit.
  Report to a HMAC Supervisor.
  Follow the directions of HMAC personnel.
  Under no circumstance re-enter facility until a HMAC management member informs you it is safe.

## Slide 5: Read & Understand Signs
07/28/26
<number>
Wellsboro Plant

## Slide 6: Lift truck operation
07/28/26
<number>
Stay in designated aisle ways.
Be aware of your surroundings.
Listen for horns and backup alarms.
Wellsboro Plant

## Slide 7
07/28/26
<number>
Safety glasses required while in plant operations.
Safety shoes while in plant operations.
Hard hats required while in a man-lift.
Hearing protection while in plant operations.
Personal Protective Equipment

## Slide 8: MSDS Communications
07/28/26
<number>
Know where to locate Material Safety Data Sheets.

## Slide 9: Health Issues
07/28/26
<number>
In case of an injury or illness
  Notify your supervisor or HMAC contact.
  See a First Responder.

## Slide 10: Lockout / Tagout
07/28/26
<number>
Lockout / tagout procedures are implemented to prevent unexpected release of energy.
All energy sources with electrical, chemical, thermal, pneumatic, hydraulic and mechanical potential must be locked and tagged out prior to work activities.

## Slide 11: Lockout / Tagout Cont.
07/28/26
<number>
Locks must be placed on equipment by the contractor’s employee and the Maintenance Department of HMAC notified of such.
Energy controls must be verified prior to working on equipment.
Removal of locks must be completed as soon as work is completed.

## Slide 12: Electrical Work
07/28/26
<number>
Each contractor must comply with: 29 CFR 1910 Subpart S, 29 CFR 1926 Subpart K, National Electric Code, Electrical Safety Requirements for Employee Workplaces (NFPA 70E), local codes and requirements, Ward/HMAC engineering standards and practices.

## Slide 13: Qualified Person/Electrical Technicians
07/28/26
<number>
Shall be capable of working safely on energized circuits and shall be familiar with the proper use of special precautionary techniques, personal protective equipment, insulating and shielding materials and insulated tools.
Shall possess the skills and techniques necessary to distinguish exposed live parts from other parts of electric equipment.

## Slide 14: Qualified Person/Electrical Technicians Cont.
07/28/26
<number>
Shall possess the skills and techniques necessary to determine the nominal voltage of exposed live parts.

## Slide 15: Electricians / Technicians required PPE as a minimum, Reference NFPA 70E:
07/28/26
<number>
Safety glasses with side shields.
Hearing protection.
Steel toed footwear
Flame retardant shirt and pants rated at 8 cal/cm2 (An untreated cotton T-shirt must be worn under Flame Retardant long sleeve shirt.
Head protection with a Class E rating.

## Slide 16: Respiratory Protection
07/28/26
<number>
Respirators shall be worn when working with or exposed to gases, vapors or dust is above the OSHA permissible levels or when required by HMAC.
Employees must be trained in care and usage of respirators.

## Slide 17: Hazardous Communication
07/28/26
<number>
Contractor is required to submit all material safety data sheets for all materials brought into facility.
Contractor must inform the Health and Safety Department of Ward/HMAC of any hazardous conditions resulting from operations conducted at the facility.

## Slide 18: Excavations
07/28/26
<number>
Excavations and trenches must be barricaded to protect pedestrians and vehicles.
All excavated material must be piled at least 3 feet from the edge of the excavation.
Depths of 5 feet or greater must be shored or sloped to eliminate the hazard of cave-in.

## Slide 19: Excavations Cont.
07/28/26
<number>
A ladder for employee exit and access must be provided.
A competent person means one who is capable of identifying existing and predictable hazards in the surroundings, or working conditions which are unsanitary, hazardous, or dangerous to employees, and who has authorization to take prompt corrective measures to eliminate them.

## Slide 20: Burning and Welding Procedures
07/28/26
<number>
All electric welding must have proper grounding.
All arcs should be shielded in production areas.
Approved welding helmet must be worn.

## Slide 21: Hot Work Permit
07/28/26
<number>
Before welding in an area where there are combustibles or flammables, a hot work permit must be obtained from the Maintenance Department of HMAC.
Hot work permits must be posted in the area where the work is being performed.
The hot work permit is only good for 1 shift.

## Slide 22: Hot Work Permit Cont.
07/28/26
<number>
A fire watch must be positioned during the welding or burning operation and 30 minutes after.
A type ABC fire extinguisher, supplied by the contractor, must be present during procedure.

## Slide 23: Confined Space Permit
07/28/26
<number>
A confined space permit must be obtained from the Health & Safety Department of Ward/HMAC prior to entry.
Contractor must present training records of employees who will be performing work.

## Slide 24: Confined Space Permit Cont.
07/28/26
<number>
The permit must be posted at the confined space entrance.
Permits are only valid for one shift.
Ground fault circuit interrupters must be used at all times.
It is the responsibility of the contractor to obtain the confined space permit.

## Slide 25: Housekeeping
07/28/26
<number>
Keep work areas neat and orderly.
Keep all emergency exits and fire extinguishers clear and unobstructed.

## Slide 26: Fall Protection
07/28/26
<number>
Fall protection is required to be worn when working at heights greater than four feet unless protected by standard handrails.
Safety belts are not acceptable as fall protection.
Safety harnesses are required in the operation of aerial lift platforms.
Inspection required prior to use.

## Slide 27: Portable Power Tools
07/28/26
<number>
Electrical cords must be double insulated or shall be of an approved system that contains three wires with a ground.
OSHA 29 CFR 1926.404 requires inspection and testing of equipment.
The use of ground fault circuit interrupters is required.

## Slide 28: Portable Power Tools Cont.
07/28/26
<number>
All guards and shields must be in place and in good condition.
All defective tools must be taken out of service immediately.

## Slide 29: Extension Cords
07/28/26
<number>
Extension cords must be of the three-wire type and protected by a ground fault interrupter or plugged into a ground fault interrupter receptacle.
Extension cords and connections must be kept away from water and damp surfaces.
OSHA 29 CFR 1926.404 requires inspection and testing of equipment.

## Slide 30: What is an Environmental Management System?
07/28/26
<number>
An EMS is-
  A systematic approach to meeting environmental requirements across an organization
Environmental requirements -
  Regulatory
  Customers and other third parties
  Parent Company
Notes: 07/28/26
<number>

## Slide 31: What is ISO 14001?
07/28/26
<number>
ISO 14000 is a series of international standards developed to provide a structure for managing environmental impacts of an organization
ISO 14001 is the internationally recognized standard for EMSs
Will be certified by third party registrar - like ISO/QS 9000
Notes: 07/28/26
<number>

## Slide 32: Why implement ISO 14001?
07/28/26
<number>
To minimize impact on the environment.
To be the best possible neighbor.
Notes: 07/28/26
<number>

## Slide 33: What are other benefits of ISO 14001?
07/28/26
<number>
Prevent pollution and minimize waste.
Conserve energy and natural resources.
Increase efficiency.
Reduce costs.
Notes: 07/28/26
<number>

## Slide 34: What are key ISO 14001 elements?
07/28/26
<number>
Environmental Policy
Environmental Impact Identification
Objectives and Targets
Written Procedures and Job Instructions
Communication & Documentation
Internal Audits
Corrective and Preventive Action
Management Review
Notes: 07/28/26
<number>

## Slide 35: How does ISO 14001 work?
07/28/26
<number>
Environmental
Policy
Checking and
Corrective Action
Continual
Improvement
Management
Review
Planning
Implementation
Notes: 07/28/26
<number>

## Slide 36: Environmental Policy
07/28/26
<number>
ENVIRONMENTAL POLICY
  Quality Products
  Satisfied Customer
  Timely Delivery
  Competitive Prices
  Continuous Improvement
  Prevent pollution
  Compliance with Requirements
  “We will continue to reduce wastes, prevent pollution and conserve energy and natural resources, helping to ensure an adequate supply for future generations.”
Notes: 07/28/26
<number>

## Slide 37: Policy - key concepts
07/28/26
<number>
Commitment to pollution prevention.
Commitment to compliance with laws and regulations.
Commitment to continuous improvement.
Notes: 07/28/26
<number>

## Slide 38: What are environmental aspects?
07/28/26
<number>
Aspect - An element of an organization’s activities, products or services that can interact with the environment
  example of activities - shipping/receiving, production, communication, waste disposal
  any and all products, including by-products that are sold
  all services provided on behalf of the company
Example - Aboveground Storage Tank
Notes: 07/28/26
<number>

## Slide 39: What are environmental impacts?
07/28/26
<number>
Impact - Any change to the environment, adverse or beneficial, resulting from an organization’s activities, products or services
  change to environment means:
    air emissions, water discharges, soil contamination
    wastes, energy and natural resource use
    excess noise, site modifications (fill or dredge)
    landscaping, clearing, paving, building
Example - Potential Tank Release
Notes: 07/28/26
<number>

## Slide 40: What are our significant impacts?
07/28/26
<number>
Generating Scrap
Air Emissions
Wastes
Energy Use
Notes: 07/28/26
<number>

## Slide 41: How do we plan to carry out the policy?
07/28/26
<number>
For each significant aspect/impact identified, we must:
  Consider developing goals to improve performance
  Measuring progress towards goals
  Control operations to minimize/prevent impacts
    procedures and work instructions
Notes: 07/28/26
<number>

## Slide 42: What are our objectives and targets?
07/28/26
<number>
Conserve energy and natural resources.
  Reduce internal scrap
  Reduce coolant use by 10%
  Improve refractory life
  Reduce disposal of general plant trash
Minimize adverse effects to air, land and water.
  Control outdoor storage areas
Meet legal requirements.
Notes: 07/28/26
<number>

## Slide 43: What are the key roles in the EMS?
07/28/26
<number>
Environmental Management Representative (EMR)
    Make sure that the EMS meets the standard
    Report EMS performance to management
Core Team
    Assist in identifying aspects and impact, objectives and targets; operational control and monitoring and measurement needs
Notes: 07/28/26
<number>

## Slide 44: How can you make a positive impact? How can you make a positive impact?
07/28/26
<number>
Follow procedures and work instructions
Housekeeping
    Use clean-up time
Proper spill response
    Contact Spill Team members
Promote environmental awareness
    At work and at home
Notes: 07/28/26
<number>

## Slide 45: Harassment
07/28/26
<number>
HMAC has a stated policy of "Zero Tolerance".
  Harassment in any form is strictly prohibited.
This includes but is not limited to:
  Verbal or physical conduct, unwelcome advances with regard to or on the basis of race, color, religion, creed, age, sex, national origin or ancestry, marital status, status of a disabled veteran, illness or handicap.
  Violation will mean an immediate suspension pending investigation and could mean an immediate termination dependent upon the severity of the act.
If harassment occurs, please contact the Human Resources Manager immediately.

## Slide 46: Reasons for Removal from Facility
07/28/26
<number>
Reporting to the facility intoxicated.
Use of illicit drugs.
Refusing to follow safety rules of the facility.
Possessing a weapon on site.

## Slide 47: Thank you and Remember
07/28/26
<number>